# Preparing the Profibus MS Card

## Overview

A new SST 5136-PBMS card has to be loaded with two software modules before it can be installed in a FieldServer x40. These software modules must be written to FLASH memory on the card:

- PBMDPSLV.SSF – DP Slave software module file

- MSLVPGA.SSP – Card PGA Configuration file

SST does not provide the source code for the Card FLASH programmer so this cannot be done on the FieldServer. The modules also cannot be loaded into Card RAM.

Unless the card can be obtained from SST preloaded with both software modules, the following procedure have to be followed:

Card Installation and FLASH programming procedure

- Set the DIP switches on the card for a default port address of 0x250 as shown below:

| Switch | Setting |
| --- | --- |
| 1 | ON |
| 2 | ON |
| 3 | OFF |
| 4 | ON |
| 5 | OFF |
| 6 | ON |

- Install the card in an empty ISA bus slot on a Windows 98 PC.

- Refer to Section 2.2 “Preparing the Computer” in the 5136-PBMS Hardware Guide and follow the procedure to setup Windows 98.

- Make a folder on the harddisk and copy the following files into the folder:

PBMDPSLV.SSF

MSLVPGA.SSP

pbmpgrm.exe

- Open a MSDOS window under Windows 98, change to the folder you created and run the following cmds:

pbmpgrm ssp=mslvpga port=250

pbmpgrm ssf=pbmdpslv port=250

- Make sure the output of both the commands indicate successful FLASH programming.

- The card is now ready for installation into a FieldServer x40.